## Slide 1
March 8, 2024
LANDFILL DEVELOPMENT FEASIBILITY
(MOSS III LANDFILL)
PRESENTER:
David K. Paylor
Vice President of Environmental
Charleston • Morgantown • Winchester, VA
Project #: 0103-22-0164
RUSSELL COUNTY
137 Highland Drive, Suite A
PO Box 1208
Lebanon, Virginia 24266

## Slide 2
RUSSELL COUNTY ENGAGED POTESTA
2
Identify Health/Safety Issues (regarding citizens)
Evaluate the Feasibility of the Site as a Landfill
Address Unique Site Features
Address Environmental Concerns
Meet/Exceed State Regulations

## Slide 3
SITE EVALUATION
3
REVIEWED FATAL FLAW SCREENING REPORT
Further Evaluation Proposed
  Stability of slopes/types of materials/dams
  Verification of limits of underground mining
  Geologic faults/seismic activity
  SITE VISIT
  Bowl-shaped depression
  Existing coal refuse
  Adjacent dams

## Slide 4
SITE EVALUATION
4
LETTER REPORT WITH RECOMMENDATIONS
No issues identified that make the site “unpermittable”
Detailed evaluation/proper technical design are critical to addressing issues identified for further assessment
  RECOMMENDATIONS
  Landfill liaison
  Leachate collection/detection layers
    Gravity flow to outside landfill
    Adequate leachate treatment plan
    Remove ponded water

## Slide 5
SITE EVALUATION
5
  RECOMMENDATIONS
    Remove unsuitable material
      Coal fine/soft soils
      Acceptable firm foundation
  Evaluate the suitability of coarse coal refuse
  Detailed Stability Analyses
    Natural soils
    Coarse coal refuse
    Existing coal refuse dam embankments
    Proposed liner system
    Landfill waste

## Slide 6
SITE EVALUATION
6
  RECOMMENDATIONS
  Mine Safety & Health Administration (MSHA)
    Approval for fills impacting Dams 1 and 2
    Evaluation of Underground Mining
      Horizontal/vertical location
      Height of mine void
      Angle of draw

## Slide 7
ADDITIONAL REQUIREMENTS
7
  Design/implement mine stabilization program
    e.g., full roof contact grouting
    Slope stability for all components
      Prepared subgrade
      Coal refuse
      Landfill liner system
      Slopes/embankments of coal refuse fills/impoundments
      Natural ground slopes (under/adjacent to landfill)
      Temporary/final slopes of landfill (waste placement, cover material)
      Material strength parameters based on sampling/laboratory analyses

## Slide 8
ADDITIONAL REQUIREMENTS
8
        Develop dewatering plan
        Evaluate bearing capacity, settlement/consolidation of subgrade, etc.
        Leachate storage
        Liner material able to elongate due to stress/strain from mine subsidence
        Meet/exceed Virginia Department of Environmental Quality Regulations

## Slide 9
SUMMARY
9
  Meet/exceed Virginia Department of Environmental Quality Regulations
  No fatal flaws identified to date
  Detailed evaluation/proper technical design are critical to addressing issues identified for further assessment